## Slide 1: Unit 1. Antennas and Free Space Propagation
ECE-GY 6023. Introduction to Wireless communications
Prof. Sundeep rangan

## Slide 2: Learning Objectives
Mathematically describe an EM wave:
  Direction of motion, wavenumber, frequency, polarization, …
Identify radio spectrum and power levels used in common commercial wireless products
Perform basic power calculations in dB scale
Perform basic mathematical operations in polar coordinates
  Conversions to cartesian coordinates, rotations, integrals, averages, …
Use tools from MATLAB to compute and plot key antenna parameters
  Directivity, gain, efficiency, …
Compute received power in an angular region using the radiation density and intensity.
Compute the free-space path loss using Friis Law
Derive Friis Law

## Slide 3: Outline
Basics of Electromagnetic Waves
Power and Bandwidth of Signals
Basics of Antennas
Free Space Propagation

## Slide 4: Electric and Magnetic Forces
Two closely related forces:
  Electric: Forces between charged particles
  Magnetic: Forces between moving charged particles
EM forces operate at a distance
  Current in one location current in another location
Enables communication
  Modulate current at a TX
  Currents create EM fields in space
  Detect modulation at a RX
TX
RX

## Slide 5: Electric and Magnetic Vector Fields
E and M forces represented by a vector field
  Changes with position and time
  Force strength has a direction and magnitude
Electric Field:
  Units: N/C (force / unit charge)
Magnetic field:
  Units: in N/(Am) = Teslas (force / unit charge / velocity)

## Slide 6: Plane Waves
EM field governed by Maxwell’s equations
In free space, all solutions can be decomposed into plane waves
EM plane wave at position
Key constraints:
  is always perpendicular to
  speed of light

## Slide 7: Visualizing Plane Waves
EM plane wave at position
At any given position :
  and fields vary sinusoidally with frequency
  Maximum amplitudes and
  Phase
For a fixed time , along direction
  and fields vary sinusoidally with wavelength
Can be viewed as traveling along direction

## Slide 8: Plane Wave Direction of Motion
Direction of motion = direction of “energy flux”
“Poynting” vector:
  = direction of motion
  Represents “energy flux”
  Energy consumed =
  Units =
  characteristic impedance
  Vacuum:

## Slide 9: Polarization
Polarization: Orientation of E-field relative to direction of motion
Linearly polarized: Constant orientation
  Vertical:
  Horizontal:
  Angular frequency and wave number
Two degrees of freedom:
  Consider any plane wave in some direction
  Can be decomposed as V + H
Also, circularly polarized
  Sum of V and H that are out of phase
  Called left hand and right hand

## Slide 10: Plane Wave Decomposition
Every electric field is a linear combination of plane waves
Each plane wave in the decomposition has:
  Frequency
  Direction of motion
  Gain, Phase
  One of two polarization
Decomposition can be found from a 4D Fourier transform
  and
  Converts time + space wavenumber and frequency
  Note that there are two polarization components
This decomposition is used in many EM solvers
  And your EM class if you take it

## Slide 11: In-Class Problem

## Slide 12: Outline
Basics of Electromagnetic Waves
Power and Bandwidth of Signals
Basics of Antennas
Free Space Propagation

## Slide 13: Signals for Communication
Signal: Any quantity that varies in time
  Continuous, discrete, complex, real, …
Signals for wireless communications:
  Modulate an information bearing signal to a signal in the EM radiation
Three key characteristics of the signal: power, bandwidth, center frequency
TX signal
Carries information
EM radiation
Antenna

## Slide 14: Energy and Power of Signals
Consider a scalar-valued, continuous-time signal
Define instantaneous power:
Typically this is proportional to the actual power
  Ex 1: For a voltage, power
  Ex 2: For an EM plane wave , power flux
Energy:
  Signal is called an “energy signal” if
Power:
  Energy per unit time
  Signal is called a “power signal” if limit exists and is finite

## Slide 15: Power: Linear and Decibel scale
Linear scale units
  Power measured in Watts (W) or mW
  Power values in W or mW called linear scale
  Energy measured in Joules (J) or mJ
Power often measured in dB scale:
  PdBW = 10log10(PW / 1W)
  PdBm = 10log10(PmW / 1mW)
  EdBmJ = 10log10(EmJ / 1mJ)
  dB scale is preferred since wireless signals have very large range
Example: P = 250 mW (typical max mobile transmit power)
  In dBW: P = 10log10(0.25W / 1W)=-6 dBW
  In dBm: P = 10log10(250mW / 1mW)=24 dBm

## Slide 16: Some important dB values
Some conversions don’t need a calculator:
  10log10(2) = 3 [Most important: Doubling power = 3dB]
  10log10(3) =4.7 ~5
  10log10(10) = 10
You can cascade these.
Ex: What is 50 mW in dBm?
Ans:

## Slide 17: Gain and Loss in dB
Linear scale: Gain is multiplication
  : TX and RX power in W or mW
  Power gain (dimensionless)
  Gain (e.g. amplifier)
  Loss (e.g. propagation, attenuator, …)
Channel power gain
TX
RX
dB scale: : Gain is addition
  : TX and RX power in dBW or dBm
  Power gain in dB
  Gain
  Loss

## Slide 18: Typical Wireless Power Transmit Levels
100 kW = 80 dBm: Typical FM radio transmission with 50 km radius
1 kW = 60 dBm: Microwave oven element (most of this doesn’t escape)
~300 W = 55 dBm: Geostationary satellite
250 mW = 24 dBm: Cellular phone maximum power (class 2)
200 mW = 23 dBm: WiFi access point
32 mW = 15 dBm: WiFi transmitter in a laptop
4 mW = 6 dBm: Bluetooth 10 m range
1 mW = 0 dBm: Bluetooth, 1 m range

## Slide 19: Example: Power and Time Calculation
Problem: Suppose that: TX power= 17 dBm, path loss= 80 dB
What is the RX power in dBm and mW?
  dB scale: dBm
  Linear scale: mW = 0.5 nW
What is the energy received in us (Symbol time for an 802.11g OFDM system):
  Linear scale: mJ
  dB Scale: Converting mJ to dB: dBmJ
Note unit: dBmJ = Energy relative to 1 mJ
Can also compute the energy directly without converting to linear scale:
  dBmJ

## Slide 20: Bandwidth and Carrier Frequency
Power density spectrum:
  PSD measures the power per unit frequency
  Indicates range of frequencies of the corresponding EM wave
  Measured by a spectrum analyzer
Two key parameters for RF signals:
  Carrier or center frequency,
  Bandwidth
Note for a real-valued signal: Always two images
0

## Slide 21: Example: PSD Calculation
Problem: Suppose that: TX power= 17 dBm, path loss= 80 dB, bandwidth = 16.25 MHz
  Assume power is transmitted uniformly over the bandwidth
  Bandwidth is the occupied BW for an 802.11g signal
What is the RX power in dBm in a 5 MHz bandwidth:
  In linear scale, RX PSD = 16.25 MHz
  RX power in MHz is
  In dB scale:

## Slide 22: Importance of Bandwidth
Data rate generally scales linearly in bandwidth
  If the transmit power and bandwidth increase by the communication rate increase by
  We will see this in detail later
Ex: Compare GSM (2G) and LTE (4G)
  Single channel of GSM system = 200 kHz
  Single channel of LTE = 20 MHz
  If power scales sufficiently, LTE would in general have 100x data rate
  LTE, in fact, can have even more capacity due to other improvements
Figure to the right: 802.11ad channels
  The channels are > 2 GHz

## Slide 23: Radio Spectrum
Image: Britanica, https://www.britannica.com/science/radio-frequency-spectrum
More bandwidth
Less Range
Less bandwidth
Greater Range

## Slide 24: Millimeter Wave Bands
New bands for 5G
  100x more bandwidth than conventional bands below 6 GHz
  Bands at 28 GHz and 38 GHz opened up by FCC
  5G systems operating have just started deployments

## Slide 25: In-Class Exercise

## Slide 26: Outline
Basics of Electromagnetic Waves
Power and Bandwidth of Signals
Basics of Antennas
Free Space Propagation

## Slide 27: Excellent Text for Antennas
This lecture is based on classic text
  Balanis, “Antenna Theory”
  Most of the figures here are from this text
If you want to learn more, study the text:
  Provides full EM theory view
  Many excellent problems and examples
  Designed for RF engineers
We will use only a small portion here
Take an EM class for more!

## Slide 28: Waveguides and Transmission Lines
Transmission lines and waveguides: Any structure to guide waves with minimal loss
Some texts:
  Transmission lines refer to conductors and waveguides to hollow structures
Many examples
Coaxial cable
Waveguide
PCB traces
Microstrip: External layer
Stripline: Internal layer

## Slide 29: Antenna
Transmit antenna: Radiates electromagnetic waves
Converts signals:
  From guided signals in transmission lines to
  To radiation in free space
Receive antenna: Collects EM wave
USRP with four vertical antenas

## Slide 30: Radiation Patterns
Aantenna radiation typically shown via a pattern
  Value of scalar as a function of position
  Antenna usually at origin
  Orientation of the antenna is important
Many possible quantities:
  Power, electric field, …
  Normalized or un-normalized
  Can be 2D or 3D
3D
2D

## Slide 31: Spherical Coordinates
Radiation patterns are often given in spherical coordinates
Polar coordinates:
  Azimuth, counter-clockwise angle in xy plane
  Inclination angle from z axis
  Radius from origin
Wireless sometimes uses elevation form:
  Use
  Measures angle from xy-plane
  Most antenna and math texts use polar form
  But MATLAB antenna toolbox uses elevation form
Remember right hand rule!
Spherical (polar form) Cartesian
Polar coordinates

## Slide 32: Spherical Coordinates in MATLAB
Conversion between spherical and cartesian
Conversion to a coordinate system

## Slide 33: Radians and Steradians
Radian:
  Circle of radius one
  Angle for unit length on circumference
  radians in the circle
Steradian
  Defined on sphere of radius one
  Angles corresponding to unit area on surface
  sr in the sphere
Infinitesimal area and solid angle:
  Note: is the inclination angle not elevation

## Slide 34: Radiation Density
Recall instantaneous energy flux for a plane wave:
  normal vector in direction of the plane wave, characteristic impedance
Typically consider fields at some frequency :
Time average power
  Note factor of 2
Can write ,
  Radiation density: radiation density
  Maximum power available if aligned in the direction
  Units
  This is a function of position

## Slide 35: Radiation Intensity
From previous slide: Radiation density:
  Units
Also define radiation intensity:
  Watts per solid angle:
In far field, radiation pattern typically decays as:
  In this case,
  Only depends on angular position
  Does not depend on distance

## Slide 36: Total Radiated Power
Total radiated power:
  Units is Watts
  Note term! Angle here is elevation angle not polar angle
Typically measured in dBm or dBW:
  Power relative to mW or W

## Slide 37: Example Problem
Problem: Total radiated power: dBm
  Assume power is uniformly radiated
  At distance of 2 km, what is the power that strikes a 1 cm x 2 cm surface?
Solution:
  Since power is uniform, radiation density is
  RX power in small area is
  Area in m^2,
  In dB scale:
2 km
dBm

## Slide 38: Isotropic Antenna
Isotropic antenna: Radiates uniformly in all directions
Radiation density and intensity are uniform
  Radiation density:
  Radiation intensity:
  Do not depend on angles
Mostly theoretical construct:
  Most real antennas have some “directivity”
In fact, there can be no coherent (linearly polarized) isotropic radiator
  E-field would be always tangent to sphere
  Such an E-field would have to go to zero in at least one point (“Hairy Ball Theorem”)
Theoretical isotropic pattern

## Slide 39: Antenna Directivity
Most real antennas concentrate power in certain angles
  They are non-isotropic
Antenna directivity:
  [dimensionless]
  Measures power at an angle relative to average
  Average in linear domain is one
  For isotropic antenna,
Max directivity:
  Directivity in direction with maximum power
Typically measured in dBi
  dB relative to isotropic
Theoretical isotropic antenna
Horn antenna with directivity

## Slide 40: Antenna Gain and Efficiency
Most antennas have losses
Define efficiency:
  Radiated to input power in TX mode
  Remaining power is lost in heat in the antenna
  Losses in the conductor and dielectric
Lossless antenna:
Antenna gain:
  Radiation intensity per unit input power
  For losses antennas, gain = directivity
Radiated power
Input power
Losses / heat

## Slide 41: Antenna Toolbox in MATLAB
Powerful routines for:
  Design and analysis of antennas
Benefits:
  Supports many antennas
  Accurate EM modeling
  Nice visualization tools
  Simple to use
Also, free to NYU students
  Just download it with MATLAB
But…very slow for complex antennas

## Slide 42: Patterns in MATLAB: Dipole Example
MATLAB has powerful tools for calculating antenna patterns

## Slide 43: Microstrip Patch Example
A more complex antenna
Many other parameters
  Substrate selection (e.g. FR4, Rogers)
  Shapes, notches, …

## Slide 44: More Complex Antennas
For complex antennas:
  MATLAB antenna toolbox is often too slow
  Cannot handle packaging, covers, obstacles, …
  Need other tools (e.g. Ansoft HFSS and CST)
Use MATLAB custom antenna object
  Store offline computed pattern
CST simulation of 28 GHz array on a handset with cover https://blogs.3ds.com/simulia/5g-antenna-design-mobile-phones/
Demo of custom antenna element in MATLAB

## Slide 45: Field Regions
Antenna patterns depend on the region
Reactive near field:
  Reactive pattern dominates
Radiating near field or Fresnel region:
  Angular pattern depends on distance
Far field or Fraunhofer region:
  Angular pattern independent of distance
  Radiation is approximately plane waves
Can be approximately calculated using:
  Maximum antenna dimension
  Wavelength

## Slide 46: Rayleigh Distance
Distance to far-field = Rayleigh distance
Most cellular / WLAN systems operate in far field
Ex 1: Half wavelength dipole antenna
  = 2.3 GHz:
  cm
Ex 2: Large cellular base station
  m, = 2.3 GHz
  m
Ex 3: MmWave wide aperture antenna
  cm, = 140 GHz
  m

## Slide 47: In-Class Exercise

## Slide 48: Outline
Basics of Electromagnetic Waves
Power and Bandwidth of Signals
Basics of Antennas
Free Space Propagation

## Slide 49: Antenna Effective Aperture
Suppose RX antenna sees incident plane wave
  Assume polarization aligned to the antenna
The effective antenna aperture (or area):
  Power density of incident wave [W / ]
  Power delivered to load at the receiver [W]
The effective area that the antenna collects
  We will see this is different than the physical aperture
will depend on the direction of arrival

## Slide 50: Aperture and Directivity
From previous slide, effective aperture is:
  Ratio of received power to incident radiation density
Aperture-directivity relation:
  True for all lossless antennas
  Proof: next slide
Consequence: Average aperture is always
  Why?
Independent of the physical size of the antenna!

## Slide 51: Proof of the Aperture-Directivity Relation
Suppose Ant 1 transmits power
Radiation density is:
Received power at Ant 2:
TX from Ant 2, the gain must be the same:
  This is a consequence of reciprocity
Hence, for any two antennas:
From simple antenna calculations for a short dipole:
  (Needs basic EM theory)

## Slide 52: Friis’ Law
Consider two lossless antennas in free space
From previous slide:
From aperture-directivity relation:
This leads to Friis’ Law (for lossless antennas):
  Path loss is proportional to
  Path loss Inversely proportional to proportional to

## Slide 53: Example: Calculating Path Loss
Suppose GHz, m, what is the omni directional path loss?
  Omni-Directional path loss is path loss without the antenna gain
This is easily done in MATLAB:

## Slide 54: Polarization Loss
Friis’ Law assumes incident wave is aligned in polarization
In general, need to consider polarization loss
Recall: polarization vector for a plane wave:
  Direction of the E-field in phasor notation
  A complex vector in 3-dim
Polarization loss factor:
  : Polarization vector of the TX wave from antenna
  : Polarization vector of the RX incident wave
  : Angle between them

## Slide 55: Example: Polarization Loss
Problem 1:
  Base station height 10m, V-polarized
  UE height 1.5m, “portrait mode”, V-polarized
  Ground distance = 50m
  What is the polarization loss in dB?
Solution:
  The E-field from the BS will be perpendicular to direction of motion
  Angle is
  Polarization loss is dB
Problem 2: What if the UE is turned to “landscape” mode?
  Now angle is
  Polarization loss is dB
Devices have to be able to received in multiple polarizations
RX wave E-field
UE ant E-field
1.5m
10m
50m
RX wave E-field
UE ant E-field

## Slide 56: Antenna Impedance and Matching
Not all power from radio may be delivered to antenna
Some is reflected back
Described by reflection coefficient
  Also referred to as
  Complex ratio of forward to reverse wave
Also described by impedance mismatch:
Fraction of power transferred:
Also given as voltage standing wave ratio (VSWR)
Ali et al, Small Form Factor PIFA Antenna Design at 28 GHz for 5G Applications, 2019

## Slide 57: Friis’ Law with Losses
Three losses in practice:
  Polarization loss
  Conductive / dielectric loss
  Impedance mismatch
Friis’ Law with lossy antennas:
  : Efficiency of antenna
  : Angle between the polarization vectors
  Note that gain is:

## Slide 58: Demo: Plotting Path Loss on a Path
Compute the path loss on a path
  TX is isotropic at the origin
  RX is micro-strip patch element. Moves along a line
MATLAB code
  Computes angles to RX
  Computes free-space omni directional path loss
  Interpolates directivity
  Adds directivity to FSPL

## Slide 59: In-Class Exercise