## Slide 1: Unit 1. Antennas and Free Space Propagation
ECE-GY 6023. Introduction to Wireless communications
Prof. Sundeep rangan

## Slide 2: Learning Objectives
Mathematically describe an EM wave:
  Direction of motion, wavenumber, frequency, polarization, …
Identify radio spectrum and power levels used in common commercial wireless products
Perform basic power calculations in dB scale
Perform basic mathematical operations in polar coordinates
  Conversions to cartesian coordinates, rotations, integrals, averages, …
Use tools from MATLAB to compute and plot key antenna parameters
  Directivity, gain, efficiency, …
Compute received power in an angular region using the radiation density and intensity.
Compute the free-space path loss using Friis Law
Derive Friis Law

## Slide 3: Outline
Basics of Electromagnetic Waves
Power and Bandwidth of Signals
Basics of Antennas
Free Space Propagation
Frames of Reference and Rotations

## Slide 4: Electric and Magnetic Forces
Two closely related forces:
  Electric: Forces between charged particles
  Magnetic: Forces between moving charged particles
EM forces operate at a distance
  Current in one location current in another location
Enables communication
  Modulate current at a TX
  Currents create EM fields in space
  Detect modulation at a RX
TX
RX

## Slide 5: Electric and Magnetic Vector Fields
E and M forces represented by a vector field
  Changes with position and time
  Force strength has a direction and magnitude
Electric Field:
  Units: N/C (force / unit charge)
Magnetic field:
  Units: in N/(Am) = Teslas (force / unit charge / velocity)

## Slide 6: Plane Waves
EM field governed by Maxwell’s equations
In free space, all solutions can be decomposed into plane waves
EM plane wave at position
Key constraints:
  is always perpendicular to
  speed of light

## Slide 7: Visualizing Plane Waves
EM plane wave at position
At any given position :
  and fields vary sinusoidally with frequency
  Maximum amplitudes and
  Phase
For a fixed time , along direction
  and fields vary sinusoidally with wavelength
Can be viewed as traveling along direction

## Slide 8: Plane Wave Direction of Motion
Direction of motion = direction of “energy flux”
“Poynting” vector:
  = direction of motion
  characteristic impedance
  Vacuum:
Represents energy flux
  Surface integral of = energy transferred into region
  Energy consumed =
  Units =

## Slide 9: Polarization
Polarization: Orientation of E-field relative to direction of motion
Linearly polarized: Constant orientation
  Vertical:
  Horizontal:
  Angular frequency and wave number
Two degrees of freedom:
  Consider any plane wave in some direction
  Can be decomposed as V + H
Also, circularly polarized
  Sum of V and H that are out of phase
  Called left hand and right hand

## Slide 10: Plane Wave Decomposition
Every electric field is a linear combination of plane waves
Each plane wave in the decomposition has:
  Frequency
  Direction of motion
  Gain, Phase
  One of two polarization
Decomposition can be found from a 4D Fourier transform
  and
  Converts time + space wavenumber and frequency
  Note that there are two polarization components
This decomposition is used in many EM solvers
  And your EM class if you take it

## Slide 11: In-Class Problem

## Slide 12: Outline
Basics of Electromagnetic Waves
Power and Bandwidth of Signals
Basics of Antennas
Free Space Propagation
Frames of Reference and Rotations

## Slide 13: Signals for Communication
Signal: Any quantity that varies in time
  Continuous, discrete, complex, real, …
Signals for wireless communications:
  Modulate an information bearing signal to a signal in the EM radiation
Three key characteristics of the signal: power, bandwidth, center frequency
TX signal
Carries information
EM radiation
Antenna

## Slide 14: Energy and Power of Signals
Consider a scalar-valued, continuous-time signal
Define instantaneous power:
Typically this is proportional to the actual power
  Ex 1: For a voltage, power
  Ex 2: For an EM plane wave , power flux
Energy:
  Signal is called an “energy signal” if
Power:
  Energy per unit time
  Signal is called a “power signal” if limit exists and is finite

## Slide 15: Power: Linear and Decibel scale
Linear scale units
  Power measured in Watts (W) or mW
  Power values in W or mW called linear scale
  Energy measured in Joules (J) or mJ
Power often measured in dB scale:
  PdBW = 10log10(PW / 1W)
  PdBm = 10log10(PmW / 1mW)
  EdBmJ = 10log10(EmJ / 1mJ)
  dB scale is preferred since wireless signals have very large range
Example: P = 250 mW (typical max mobile transmit power)
  In dBW: P = 10log10(0.25W / 1W)=-6 dBW
  In dBm: P = 10log10(250mW / 1mW)=24 dBm

## Slide 16: Some important dB values
Some conversions don’t need a calculator:
  10log10(2) = 3 [Most important: Doubling power = 3dB]
  10log10(3) =4.7 ~5
  10log10(10) = 10
You can cascade these.
Ex: What is 50 mW in dBm?
Ans:

## Slide 17: Gain and Loss in dB
Linear scale: Gain is multiplication
  : TX and RX power in W or mW
  Power gain (dimensionless)
  Gain (e.g. amplifier)
  Loss (e.g. propagation, attenuator, …)
Channel power gain
TX
RX
dB scale: : Gain is addition
  : TX and RX power in dBW or dBm
  Power gain in dB
  Gain
  Loss

## Slide 18: Typical Wireless Power Transmit Levels
100 kW = 80 dBm: Typical FM radio transmission with 50 km radius
1 kW = 60 dBm: Microwave oven element (most of this doesn’t escape)
~300 W = 55 dBm: Geostationary satellite
250 mW = 24 dBm: Cellular phone maximum power (class 2)
200 mW = 23 dBm: WiFi access point
32 mW = 15 dBm: WiFi transmitter in a laptop
4 mW = 6 dBm: Bluetooth 10 m range
1 mW = 0 dBm: Bluetooth, 1 m range

## Slide 19: Example: Power and Time Calculation
Problem: Suppose that: TX power= 17 dBm, path loss= 80 dB
What is the RX power in dBm and mW?
  dB scale: dBm
  Linear scale: mW = 0.5 nW
What is the energy received in us (Symbol time for an 802.11g OFDM system):
  Linear scale: mJ
  dB Scale: Converting mJ to dB: dBmJ
Note unit: dBmJ = Energy relative to 1 mJ
Can also compute the energy directly without converting to linear scale:
  dBmJ

## Slide 20: Bandwidth and Carrier Frequency
Power density spectrum:
  PSD measures the power per unit frequency
  Indicates range of frequencies of the corresponding EM wave
  Measured by a spectrum analyzer
Two key parameters for RF signals:
  Carrier or center frequency,
  Bandwidth
Note for a real-valued signal: Always two images
0

## Slide 21: Example: PSD Calculation
Problem: Suppose that: TX power= 17 dBm, path loss= 80 dB, bandwidth = 16.25 MHz
  Assume power is transmitted uniformly over the bandwidth
  Bandwidth is the occupied BW for an 802.11g signal
What is the RX power in dBm in a 5 MHz bandwidth:
  In linear scale, RX PSD = 16.25 MHz
  RX power in MHz is
  In dB scale:

## Slide 22: Importance of Bandwidth
Data rate generally scales linearly in bandwidth
  If the transmit power and bandwidth increase by the communication rate increase by
  We will see this in detail later
Ex: Compare GSM (2G) and LTE (4G)
  Single channel of GSM system = 200 kHz
  Single channel of LTE = 20 MHz
  If power scales sufficiently, LTE would in general have 100x data rate
  LTE, in fact, can have even more capacity due to other improvements
Figure to the right: 802.11ad channels
  The channels are > 2 GHz

## Slide 23: Radio Spectrum
Image: Britanica, https://www.britannica.com/science/radio-frequency-spectrum
More bandwidth
Less Range
Less bandwidth
Greater Range

## Slide 24: Millimeter Wave Bands
New bands for 5G
  100x more bandwidth than conventional bands below 6 GHz
  Bands at 28 GHz and 38 GHz opened up by FCC
  5G systems operating have just started deployments

## Slide 25: Next Frontier: Upper Mid-Band
7 GHz
24 GHz
FR1 sub-6 Traditional cellular
Challenges with FR3
Wide bandwidth
Incumbents
Need for robustness
FR2 mmWave Introduced in 5G
FR3 Upper Mid-band Potential 5G-Adv and 6G
More spectrum
Better coverage
Balance of coverage & spectrum
Satellite
RADAR
Malicious jammers

## Slide 26: In-Class Exercise

## Slide 27: Outline
Basics of Electromagnetic Waves
Power and Bandwidth of Signals
Basics of Antennas
Free Space Propagation
Frames of Reference and Rotations

## Slide 28: Excellent Text for Antennas
This lecture is based on classic text
  Balanis, “Antenna Theory”
  Most of the figures here are from this text
If you want to learn more, study the text:
  Provides full EM theory view
  Many excellent problems and examples
  Designed for RF engineers
We will use only a small portion here
Take an EM class for more!

## Slide 29: Waveguides and Transmission Lines
Transmission lines and waveguides: Any structure to guide waves with minimal loss
Some texts:
  Transmission lines refer to conductors and waveguides to hollow structures
Many examples
Coaxial cable
Waveguide
PCB traces
Microstrip: External layer
Stripline: Internal layer

## Slide 30: Antenna
Transmit antenna: Radiates electromagnetic waves
Converts signals:
  From guided signals in transmission lines to
  To radiation in free space
Receive antenna: Collects EM wave
USRP with four vertical antenas

## Slide 31: Spherical Coordinates
Radiation patterns are often given in spherical coordinates
Polar coordinates:
  Azimuth, counter-clockwise angle in xy plane
  Inclination angle from z axis
  Radius from origin
Wireless sometimes uses elevation form:
  Use
  Measures angle from xy-plane
  Most antenna and math texts use polar form
  But MATLAB antenna toolbox uses elevation form
Remember right hand rule!
Spherical (polar form) Cartesian
Polar coordinates

## Slide 32: Spherical Vector Fields
A vector field: vector function of space
In spherical coordinates:
  May also write for the unit vectors
Orthogonal transformation:

## Slide 33: Spherical Coordinates in MATLAB
Conversion between spherical and cartesian
Conversion to a coordinate system

## Slide 34: Fields from an Infinitesimal Current Source
Consider infinitesimal dipole of length
  Current is at frequency
It can be shown that in the far-field (see Balanis):
  Magnetic field (direction )
  Electric field (direction )
  Poynting vector:
Notes:
  is inclination angle in above formulae
  and decay as and are tangent to the sphere
  decays at and is outward normal to the sphere
The fields for any antenna:
  Can be computed by integrating the current density

## Slide 35: Radiation Patterns
Aantenna radiation typically shown via a pattern
  Value of scalar as a function of position
  Antenna usually at origin
  Orientation of the antenna is important
Many possible quantities:
  Power, electric field, …
  Normalized or un-normalized
  Can be 2D or 3D
3D
2D

## Slide 36: Radiation Density
Each infinitesimal current source contributes Poynting vector:
Integrating the currents across the antenna we have (in far-field):
Radiation density: radiation density
  Power radiating outward from the sphere
  Units
  This is a function of position

## Slide 37: Radians and Steradians
Radian:
  Circle of radius one
  Angle for unit length on circumference
  radians in the circle
Steradian
  Defined on sphere of radius one
  Angles corresponding to unit area on surface
  sr in the sphere
Infinitesimal area and solid angle:
  Note: is the inclination angle not elevation

## Slide 38: Radiation Intensity
From previous slide: Radiation density:
  Units
Also define radiation intensity:
  Watts per solid angle:
In far field, radiation pattern typically decays as:
  In this case,
  Only depends on angular position
  Does not depend on distance

## Slide 39: Total Radiated Power
Total radiated power:
  Units is Watts
  Note term! Angle here is elevation angle not polar angle
Typically measured in dBm or dBW:
  Power relative to mW or W

## Slide 40: Example Problem
Problem: Total radiated power: dBm
  Assume power is uniformly radiated
  At distance of 2 km, what is the power that strikes a 1 cm x 2 cm surface?
Solution:
  Since power is uniform, radiation density is
  RX power in small area is
  Area in m^2,
  In dB scale:
2 km
dBm

## Slide 41: Isotropic Antenna
Isotropic antenna: Radiates uniformly in all directions
Radiation density and intensity are uniform
  Radiation density:
  Radiation intensity:
  Do not depend on angles
Mostly theoretical construct:
  Most real antennas have some “directivity”
In fact, there can be no coherent (linearly polarized) isotropic radiator
  E-field would be always tangent to sphere
  Such an E-field would have to go to zero in at least one point (“Hairy Ball Theorem”)
Theoretical isotropic pattern

## Slide 42: Antenna Directivity
Most real antennas concentrate power in certain angles
  They are non-isotropic
Antenna directivity:
  [dimensionless]
  Measures power at an angle relative to average
  Average in linear domain is one
  For isotropic antenna,
Max directivity:
  Directivity in direction with maximum power
Typically measured in dBi
  dB relative to isotropic
Theoretical isotropic antenna
Horn antenna with directivity

## Slide 43: Antenna Gain and Efficiency
Most antennas have losses
Define efficiency:
  Radiated to input power in TX mode
  Remaining power is lost in heat in the antenna
  Losses in the conductor and dielectric
Lossless antenna:
Antenna gain:
  Radiation intensity per unit input power
  For losses antennas, gain = directivity
Radiated power
Input power
Losses / heat

## Slide 44: Antenna Toolbox in MATLAB
Powerful routines for:
  Design and analysis of antennas
Benefits:
  Supports many antennas
  Accurate EM modeling
  Nice visualization tools
  Simple to use
Also, free to NYU students
  Just download it with MATLAB
But…very slow for complex antennas

## Slide 45: Patterns in MATLAB: Dipole Example
MATLAB has powerful tools for calculating antenna patterns

## Slide 46: Microstrip Patch Example
A more complex antenna
Many other parameters
  Substrate selection (e.g. FR4, Rogers)
  Shapes, notches, …

## Slide 47: More Complex Antennas
For complex antennas:
  MATLAB antenna toolbox is often too slow
  Cannot handle packaging, covers, obstacles, …
  Need other tools (e.g. Ansoft HFSS and CST)
Use MATLAB custom antenna object
  Store offline computed pattern
CST simulation of 28 GHz array on a handset with cover https://blogs.3ds.com/simulia/5g-antenna-design-mobile-phones/
Demo of custom antenna element in MATLAB

## Slide 48: Field Regions
Antenna patterns depend on the region
Reactive near field:
  Reactive pattern dominates
Radiating near field or Fresnel region:
  Angular pattern depends on distance
Far field or Fraunhofer region:
  Angular pattern independent of distance
  Radiation is approximately plane waves
Can be approximately calculated using:
  Maximum antenna dimension
  Wavelength

## Slide 49: Rayleigh Distance
Distance to far-field = Rayleigh distance
Most cellular / WLAN systems operate in far field
Ex 1: Half wavelength dipole antenna
  = 2.3 GHz:
  cm
Ex 2: Large cellular base station
  m, = 2.3 GHz
  m
Ex 3: MmWave wide aperture antenna
  cm, = 140 GHz
  m

## Slide 50: In-Class Exercise

## Slide 51: Outline
Basics of Electromagnetic Waves
Power and Bandwidth of Signals
Basics of Antennas
Free Space Propagation
Frames of Reference and Rotations

## Slide 52: Antenna Effective Aperture
Suppose RX antenna sees incident plane wave
  Assume polarization aligned to the antenna
The effective antenna aperture (or area):
  Power density of incident wave [W / ]
  Power delivered to load at the receiver [W]
The effective area that the antenna collects
  We will see this is different than the physical aperture
will depend on the direction of arrival

## Slide 53: Aperture and Directivity
From previous slide, effective aperture is:
  Ratio of received power to incident radiation density
Aperture-directivity relation:
  True for all lossless antennas
  Proof: next slide
Consequence: Average aperture is always
  Why?
Independent of the physical size of the antenna!

## Slide 54: Reciprocity of Antennas
To prove aperture-directivity, we need reciprocity
Loosely stated: Channel between antennas in both directions are equal
Mathematically:
  If Ant 1 Transmits: RX voltage / TX current
  If Ant 2 Transmits: RX voltage / TX current
  Reciprocity:
Can show that with the same loads:
  Power transfer in both directions are equal:
Antenna 1
Antenna 2

## Slide 55: Proof of the Aperture-Directivity Relation
Suppose Ant 1 transmits power
Radiation density is:
Received power at Ant 2:
TX from Ant 2, the gain must be the same:
  This is a consequence of reciprocity
Hence, for any two antennas:
From simple antenna calculations for a short dipole:
  (Needs basic EM theory)

## Slide 56: Friis’ Law
Consider two lossless antennas in free space
From previous slide:
From aperture-directivity relation:
This leads to Friis’ Law (for lossless antennas):
  Path loss is proportional to
  Path loss Inversely proportional to proportional to

## Slide 57: Example: Calculating Path Loss
Suppose GHz, m, what is the omni directional path loss?
  Omni-Directional path loss is path loss without the antenna gain
This is easily done in MATLAB:

## Slide 58: Polarization
We know E-field in far-field behaves as:
  Since E-field decays at and is tangent to the sphere
We call:
  vertical E-field pattern
  horizontal E-field pattern
Define complex gain patterns:
  and
Define polarization vector:
  Vector is in direction of E-field
  Then directivity is:
  This convention is used in Nvidia Sionna

## Slide 59: Complex Channel Gain
Friis’ Law:
  Provides power gain, not complex channel
  Assumes aligned polarization
To compute complex channel gain for arbitrary polarization
  Find angle of departure at TX:
  Find angle of arrival at RX:
  Find TX complex gain patterns:
  Find RX complex gain patterns:
Complex channel gain will be:
TX
RX
Inner product

## Slide 60: Polarization Loss
From previous slide, complex channel gain is:
Power gain is:
Define polarization unit vectors:
Since :
Polarization loss: loss due misalignment in polarization
  Often quoted in dB:

## Slide 61: Ex: Rotation Orthogonal to Path Direction
Consider two antennas:
  TX at , RX at . Both vertically polarized
TX: AoD .
  H-field is in direction
  E-field & TX pol vector
RX antenna is rotated around axis by
  AoA relative to antenna:
  H-field is in direction
  E-field & RX pol vector
  Path loss =
TX
RX
Polarization vectors aligned
Boresight not aligned
  Rotation along axis orthogonal to path direction causes no polarization loss

## Slide 62: Ex: Rotation Around Path Direction
Consider two antennas:
  TX at , RX at . Both vertically polarized
TX: AoD .
  H-field is in direction
  E-field & TX pol vector
RX antenna is rotated around axis by
  AoA relative to antenna:
  H-field is in direction
  E-field & RX pol vector
  Path loss =
TX
RX
Polarization vectors not aligned
Boresight aligned
  Rotation around axis of path direction causes polarization loss

## Slide 63: Antenna Impedance and Matching
Not all power from radio may be delivered to antenna
Some is reflected back
Described by reflection coefficient
  Also referred to as
  Complex ratio of forward to reverse wave
Also described by impedance mismatch:
Fraction of power transferred:
Also given as voltage standing wave ratio (VSWR)
Ali et al, Small Form Factor PIFA Antenna Design at 28 GHz for 5G Applications, 2019

## Slide 64: Friis’ Law with Losses
Three losses in practice:
  Polarization loss
  Conductive / dielectric loss
  Impedance mismatch
Friis’ Law with lossy antennas:
  : Efficiency of antenna
  : Angle between the polarization vectors
  Note that gain is:

## Slide 65: In-Class Exercise

## Slide 66: Outline
Basics of Electromagnetic Waves
Power and Bandwidth of Signals
Basics of Antennas
Free Space Propagation
Frames of Reference and Rotations

## Slide 67: Frames of Reference
Antenna patterns are usually given in a “local” frame of reference
  A coordinate system in a fixed relation with the antenna structure
  Ex: Coordinate aligned to the normal of a patch antenna
But antenna may have arbitrary alignment to the rest of environment
  Ex, Base station antenna tilt and orientation
Alignment may move over time
  Ex: Rotation or translation of a handset
Environment typically specified in “global” frame of reference
This section:
  How to represent local and global coordinate systems
  How to translate between the two

## Slide 68: Rigid Body
Rigid body: Any structure with fixed relative distances
  Body may be in motion
  Ex: Handset, base station antenna, antenna mounted on a car, …
Rigid body’s configuration described by two properties
Position of some reference point in the body:
Orientation around that point:
  Described by orthonormal vectors
Motion: Change of position and orientation over time

## Slide 69: Frames of Reference for Antennas
Global frame of reference: An arbitrary coordinate system, typically fixed
  Assume aligned at the origin with basis
Body or local frame of reference:
  A coordinate system for a rigid body possibly in motion
  Translation and basis in the global basis
Antenna systems
  Typ. Given antenna patterns in local frame of reference
  Signal paths given in global frame of reference
  Need to translate global to local

## Slide 70: Euler Angles
Rotation matrices in are typically described by three Euler angles
Robotics naming:
  Yaw : Rotation round axis, corresponds to azimuth angle
  Pitch : Rotation round axis, corresponds to inclination angle
  Roll : Rotation around axis
Rotation matrix given by a product
  Note order matters. Many different conventions. This product is XYZ:
https://en.wikipedia.org/wiki/Rotation_matrix
https://en.wikipedia.org/wiki/Euler_angles

## Slide 71: Computing Rotation Matrices in MATLAB
MATLAB has many tools to compute rotation matrices
Eul2rotm:
  Give angles in radians
  Give order, e.g. ‘ZYX’
See demo in github

## Slide 72: Example: Frame of Reference of a Moving Object
See MATLAB demo
Object moving in 3D space (e.g., UAV)
Antenna pointed in direction of motion

## Slide 73: Find Angles of Arrival along Path
Find the angles in RX frame of reference
RX facing TX
RX away from TX
RX above TX

## Slide 74: Find Gain along Path
Compute omni-directional path loss and gain along path

## Slide 75: Computing the Polarization Loss
Compute the E-field H and V patterns
Then perform interpolation on path
  Code for interpolation in demo
  Not shown on slide due to space
Assume TX is V pol
RX polarization vector:
  Unit vector in direction of E-field
Use MATLAB built-in polloss function
  Computes angle between TX and RX pol vectors
  Accounts for rotation of TX and RX

## Slide 76: Polarization Loss
In this case, loss is minimal
Loss is ~0.01 dB
Minimal rotation around path direction