## Slide 1: Non-LOS Propagation and Link Budget Analysis
Wireless short course
Prof. Sundeep rangan

## Slide 2: Learning Objectives
Perform simple noise and interference calculations
Define key communication requirements
  BER, BLER, information rate, spectral efficiency, bandwidth
  SNR: Energy per bit and energy per symbol
Estimate rate based on simple models or from link curves
Perform simple link budget calculations
Qualitatively describe various propagation mechanisms in real world settings
Compute reflected power from the radar equation
Generate samples from a statistical path loss model
Compute rate and SNR distributions using a statistical path loss model

## Slide 3: Outline
Noise and Interference
Communication Requirements and Link Budget Analysis
Non-LOS Propagation
Statistical Models for Path Loss
Demo: Estimating Rates with a 3GPP model

## Slide 4: What is Noise?
Noise: Any unwanted component of the signal
Key challenge in communication:
  Estimate the transmitted signal in the presence of noise

## Slide 5: Types of “Noise”
Internal / thermal noise:
  From imperfections in the receiver
  Thermal noise: From random fluctuations of electrons
  Other imperfections: Phase noise, quantization, channel estimation errors
External Interference
  Signals from other sources
  In-band: Transmitters in the same frequency Ex: Multiple devices in a cellular band
  Out-of-band: From leakage out of carrier
  Some texts do not consider “interference” as noise

## Slide 6: Thermal Noise
Thermal noise: Caused by random fluctuations of electrons
  Typically modeled as AWGN with power spectral density
Units:
  Linear scale = W/Hz = Joules
  Represents energy per degree of freedom = noise energy in any orthogonal sample
  Often written in dB scale: [dBm/Hz]
Fundamental limit determined by statistical physics:
  = Boltzman constant, temperature in Kelvin
  At room temperature (=300 K), dBm/Hz
Practical systems see higher noise power due to receiver imperfections
  Noise figure
  Typical values are 2 to 9 dB in most wireless systems

## Slide 7: NF for Cascade of Elements
Most receivers are built with multiple stages
  Each stage has a gain and noise figure
  Some stages (typically amplifiers) add noise with a noise figure
Total noise figure given by:
  With large initial gain (), init noise figure () is dominant. Must make small.
  Hence usual first stage is a low noise amplifier (LNA)
Gain G1
Thermal noise 1
kTB x NF1
Input power
Pin
Gain stage 1
G2
Additional noise
kTB (NF2-1)
Stage 2
G3
Additional noise
kTB (NF3-1)
Stage 3
Output power
Pout

## Slide 8: Example Problem Molisch 3.1
What is total NF and gain?
Answer: Compute G and NF (in linear units) for each stage:
  Attenuator: NF1=1 (does not add noise), G1=10-0.1(1.5)=0.707 (note sign)
  LNA: NF2=100.1(4)=2.51, G2=10-0.1(10)=10
  Mixer: NF3=100.1(1)=1.25, G3=1 (unit gain)
  Total gain: dB
  Noise figure dB
Attn connector
Loss = 1.5 dB
Low noise amp
Gain = 10 dB, NF = 4 dB
Mixer
Unit gain, NF = 1 dB
Gain G1
Gain G2
NF1
NF2
Gain G3
NF3

## Slide 9: Interference
Signals from other transmitters using same band and same time.
Fundamental to the broadcast nature of the wireless medium.
Adds to total noise seen at receiver
Example:
  A transmits to B (desired signal)
  C transmits to D (desired signal)
  But B gets interference from A
Desired signal
Interference
Desired
A
B
C
D

## Slide 10: Interference Calculations
Remember: Noise and interference powers add in linear scale (not in dB)!
Example:
  NF = 4 dB, B = 20 MHz
  Interference power = -95 dBm, RX signal power = -80 dBm
  Find the SNR=signal to noise and SINR = signal to interference + noise
Solution:
  Thermal noise density dBm/Hz
  Noise power In dBm: dBm
  SNR = -80 – (-97) = 17 dB
  Noise + interference power, dBm
  Note: You add in linear scale first before converting to dB!!
  SINR = -80 – (-92.9) = 12.9 dB

## Slide 11: Outline
Noise and Interference
Communication Requirements and Link Budget Analysis
Non-LOS Propagation
Statistical Models for Path Loss
Demo: Estimating Rates with a 3GPP model

## Slide 12: Communication Requirements
Basic tradeoff in all communication systems:
  Information rate: Amount of information we try to send
  Bandwidth: Spectrum the signal occupies
  Reliability: The probability it is received correctly
  Channel quality: Typically measured by the signal to noise ratio
Will review some basic concepts from digital communication:
  How are these exactly measured?
  What is the tradeoff in practical communication systems?
RX
Info rate
TX
Channel gain
Noise PSD
TX power , BW
RX power

## Slide 13: Review: Typical Transmitter Steps
Communication systems typically use three stages
  Channel coding: ex. Convolutional, turbo, LDPC
  Modulation: QPSK, 16-QAM, 64-QAM, …
  Pulse shaping
Determines modulation + coding scheme (MCS)
Info bits Rate =
Coded bits
Channel coding rate
Modulation sym/sec
Complex symbols
DAC + filtering excess BW frac
Baseband
analog
Upconversion
+ Power amp
Power

## Slide 14: Information Rate and Bandwidth
Information rate: [bits/sec]
Signal bandwidth: [Hz]
Occupied bandwidth: [Hz]
Spectral efficiency (Units are bps/Hz or bits/DOF)
Ex: A system transmits with rate ½ coding, 16-QAM, 10 Msym/s and excess BW 10%
  Data states: ; (16-QAM); Msym/s;
  Hence information rate is Mbps
  Occupied bandwidth = MHz
Info bits Rate =
Coded bits
Channel coding rate
sym/sec bits/sym
Complex symbols
DAC + filtering excess BW frac
Baseband
analog
Upconversion
+ Power amp
Power

## Slide 15: Reliability: BER and BLER
Most communication system TX data into blocks
  Framing may be used for coding, MAC layer transport blocks or IP layer
  Range in size from 100s to > 10000 bits per blocks
Measure reliability by either:
  BER: Bit error rate = fraction of bits in error (useful when there is no blocks)
  BLER: Block error rate = fraction of blocks that have at least one error
Errors typically need to be corrected at some higher layer
  Retransmissions / ARQ at MAC or transport layer (A lot more on this later!)
  Corrected by application (e.g. voice masking in audio)
Acceptable level for BER and BLER depend on many MAC and application layer factors
TX
RX
TX bits in coding blocks
RX bits in coding blocks
Error

## Slide 16: SNR and Power Relations
Power relations
  Power at receiver is
  Noise energy per degree of freedom = Noise PSD:
Channel quality is measured by SNR = signal to noise ratio
  SNR per bit (pronounced “ebb-no”)
  SNR per symbol:
Requirement will depend on the MCS used and the quality of the receiver
TX symbols
DAC+ TX filter
Upconversion
ADC +
RX filter
RX symbols
Symbol rate=
Equalization, demod,
decoding
Info bits
Estimated bits
Coding + modulation
Down-conversion
Pathloss
Rate
+
Noise PSD

## Slide 17: Example Problem
A system uses:
  Convolutional code shown () and , 16-QAM
  Symbol rate Msym/s. No excess bandwidth
  Transmit power: 23 dBm
  RX noise PSD: -170 dBm/Hz (including NF)
For a BER of find the maximum path loss
Solution:
  From graph we need dB
  Information rate is Mbps
  .
  In dB scale: dBm
  Hence, max path loss is dB
From Proakis

## Slide 18: Shannon Capacity
Capacity = max rate achievable given bandwidth and SNR
  Rate optimized over all possible MCSs and communication schemes.
Given by classic Shannon formula
Capacity relates theoretical rate to two key parameters:
  B = bandwidth in Hz
  SNR in linear scale (not dB!!!)
Mathematical result from classic paper in 1948.

## Slide 19: Bandwidth and Power-Limited Regions
Shannon formula:
Power-Limited region:
  As
  Rate linearly increases with power / SNR
Bandwidth-limited region:
  For large SNR,
  Linearly increases in bandwidth,
  Logarithmically increase in SNR.
  Increasing SNR has little practical value

## Slide 20: Actual Rate vs. Shannon Capacity
Theoretical Shannon capacity cannot be achieved
  Needs infinite computation and delay.
Practical modems achieve a rate below Shannon limit.
Useful model:
  D=fraction overhead
  b=loss factor, usually quoted in dB
  Often say “system is b dB below capacity”
  can be thought of as an “effective” SNR
Usually loss from capacity is at least 3dB
  Often higher depending on receiver complexity and other factors

## Slide 21: Rate vs. Capacity Example
What is the maximum rate for a system:
  20% overhead, 10 MHz bandwidth, SNR=12 dB
  Operates at 3dB below Shannon capacity
Answer:
  Effective SNR: dB. In linear scale (since 9=3(3))
  Therefore, Mbps
  Note the final units are in Mbps

## Slide 22: Example Link Budget
Link budget: Measures final SNR as a function of TX power and all impairments
Item | Value | Remarks
Transmit power (dBm) | 23.0 | 200 mW transmitter
Distanced based path loss (dB) | 90.0 | Will depend on propagation model
Shadowing (dB) | 20.0 | Will depend on obstructions
Receive power (dBm) | -87.0 | TX power - path loss - shadowing
Bandwidth (MHz) | 20.0 | BW of 802.11 signal
Noise figure | 5.0 | Will depend of implementation of receiver
Noise power (dBm) | -96.0 | -174 +10log(BW) + NF
SNR (dB) | 9.0 | RX pow - Noise pow

## Slide 23: Example: Rate in Free Space
Parameters similar to small cell transmission
Can get data rate of 5 km!
Since we assume free-space
  Will be much worse in reality

## Slide 24: Outline
Noise and Interference
Communication Requirements and Link Budget Analysis
Non-LOS Propagation
Statistical Models for Path Loss
Demo: Estimating Rates with a 3GPP model

## Slide 25: Reflections and Refractions
Occur at any dielectric interface
  Change in characteristic impedance
Consider two separate polarizations
  Parallel and perpendicular
Reflected components
  : Reflects in opposite angle
Refracted / transmission component:
  May be no components
Complex gains on each component
Polarization may in general change
Sean Hum, Lecture Notes, U of Toronto

## Slide 26: Metal Reflectors
Special case of a perfect conductor:
All signal is reflected back:
No transmission component:
Polarization direction is unchanged
Sean Hum, Lecture Notes, U of Toronto

## Slide 27: Transmission Through Typical Materials
Radio waves can transmit through materials, but with attenuation
Source: City of Cumberland, Maryland WiFi study
Building Material | 2.4 GHz Attenuation
Solid Wood Door1. 75" | 6 dB
Steel Fire/Exit Door 1.75" | 13 dB
Steel Fire/Exit Door 2.5" | 19 dB
Brick 3.5" | 6 dB
Concrete Wall 18" | 18 dB
Glass Divider 0.5" | 12 dB
Interior Solid Wall 5" | 14 dB
Marble 2" | 6 dB
Exterior Double Pane Coated Glass 1" | 13 dB
Exterior Single Pane Window 0.5" | 7 dB

## Slide 28: Attenuation Models in MATLAB
MATLAB Phased Array Toolbox has many models atmospheric attenuation
  Commands for free space path loss, and attenuation for fog, gas and rain
  Based on well-studied measurements
Note: Water absorption is particularly important to model for mmWave!

## Slide 29: Specular Reflections & Scattering
Due to surface roughness, reflected radio waves can be scattered in many directions.
Amount of power loss in specular component related to height of surface irregularities.
Texts provides probabilistic models to estimate power loss based on random height variations.

## Slide 30: Radar Cross Section
Intuition:
  Let incident radiation density
  Reflect total power =
  effective area captured for reflection
  Scattered density is:
Define radar cross section:
Defines effective area of receiving target
Generally depends on angle

## Slide 31: Radar Equation
Radar Equation: Ratio of RX to TX power
  Proof: Next slide
Provides basic equation for radar link budgets
Key points:
  Power decays as
  Much faster than LOS free-space
  Remember directivity and RCS depend on angle

## Slide 32: Proof of the Radar Equation
Incident density:
Reflected density:
Received power
Using antenna-directivity relation:
Therefore:

## Slide 33: Typical RCS Values
Values are often quoted in dBsm
From Balanis
From RFCafe
Note formulas only true valid in optical range:
Range
Area

## Slide 34: Example: RCS of a UAV
Measurements of RCS of commercial UAVs
  Use an anechoic chamber (removes reflections)
Notice RCS is much larger when facing the drone
Very small when seeing drone from side
From Semkin, Vasilii, et al. "Analyzing Radar Cross Section signatures of diverse drone models at mmWave frequencies." IEEE Access (2020).

## Slide 35: Propagation Loss with Reflections
In free space, we saw power density decays as
Due to ground reflections, power decays faster than
For d large, decays as = path loss exponent.
  a has been observed from 1.5 to 5.5, but usu. btw 3 and 5.
For single ground reflection, can show =4.
  Based on reflected wave canceling direct wave
  See www.wiley.com/go/molisch Appendix 4-A

## Slide 36: Path Loss Exponent, Coverage & Interference
For coverage-limited systems, low a is good
  Power decays slower => signals have greater range
For interference-limited systems, high a is good
  Ex: If thermal noise is negligible:
Desired signal
Dist = d1
Interfering signal
Dist = d2
P1
P2

## Slide 37: Diffraction
Interfering objects (IOs) do not result in sharp shadows.
  Due to wave nature of EM radiation
  Simple ray model is not correct.
Waves diffract at IO boundaries,
  Intensity after IO can be stronger in parts than with no IO!

## Slide 38: Human Blocking at 73GHz Example
0.5 m
1.0 m
1.5 m
2.0 m
2.5 m
3.0 m
3.5 m
4.0 m
4.5 m
5 m
TX
RX
41
42
43
44
45
46
47
48
49
G. R. MacCartney, Jr., S. Deng, S. Sun, and T. S. Rappaport, “73 GHz Millimeter-Wave Human Blockage and Dynamic Measurements,” IEEE VTC 2016
Between 25 and 40 dB blockage
  Depends on distance
Total power predicted by knife edge diffraction
Piecewise linear model used by 3GPP

## Slide 39: Radio Waves Have Many Paths

## Slide 40: Outline
Noise and Interference
Communication Requirements and Link Budget Analysis
Non-LOS Propagation
Statistical Models for Path Loss
Demo: Estimating Rates with a 3GPP model

## Slide 41: Real Path Loss
Path loss is a complex function of environment
Varies with distance, obstacles, reflections …
Site specific path loss can be predicted with ray tracing
Outputs of commercial WinProp ray tracer

## Slide 42: Statistical Path Loss Models
Model path loss as a random variable
Environmental effects are modeled as random
Model fit for a type of environment
  Eg. Urban, suburban, indoor, … Not site-specific
Based on data
Used for evaluation of performance statistics
  Coverage, rate distribution, …

## Slide 43: Linear Models
Floating intercept model:
  Parameters , fit from data
Used widely in 3GPP, IEEE
  Different models for different scenarios
Caution in any fit model:
  Do not use outside distances, frequencies it was derived
NLOS
LOS
Distance (log scale)
Path loss (dB)

## Slide 44: Related Models
Close in (CI) model
  Match free space at some fixed reference distance
  One less parameter to fit
  Matches true path loss at
Hata model, ….
Multi-slope models
3GPP NLOS / LOS hybrid models

## Slide 45: Outage Probability
Consider transmission with fixed MCS with rate
  No adaptation!
Requires
  Outage: Event that
  Results in zero rate
With variable path loss, , is a random variable
Outage probability:

## Slide 46: Outline
Noise and Interference
Communication Requirements and Link Budget Analysis
Non-LOS Propagation
Statistical Models for Path Loss
Demo: Estimating Rates with a 3GPP model

## Slide 47: Ex: 3GPP Indoor Home Office Model
3GPP has models for many statistical models
  38.900: Path loss models for above 6 GHz
Example: Indoor home office
  Separate models for LOS and NLOS
  Plotted is the median path loss vs. distance

## Slide 48: Ex: Probability of LOS
Model has a probability of LOS
Function of distance
  As distance is larger, probability of LOS is smaller

## Slide 49: Ex: Generating Random Samples
The full model generate random path loss
  Path loss is a function of distance
  Samples from the conditional distribution
Steps:
  Compute median LOS and NLOS path loss
  Add shadowing
  Randomly select between LOS and NLOS
  Use PLOS probability

## Slide 50: Example Simple Simulation
Simulations: Often used to estimate distribution of rates
  Assume some statistical distribution on locations and propagation
Illustrate with a simple simulation
  RX is randomly located in a square region.
  TX is located at origin
3GPP has much more realistic deployment models
TX

## Slide 51: Generate Random Path Loss
Generate random path losses based on distances

## Slide 52: Compute SNR Distribution
Make assumptions similar to an 802.11ad-like system
  We assume very directive antennas
  Later we show how to do this with beamforming

## Slide 53: Compute Rate Distribution
Compute rate distribution assuming simple backoff from Shannon capacity
  More realistic models are possible
Note the large range of rates in this region