## Slide 1: Unit 8. Multiple Antennas and Beamforming
EL-GY 6023. Wireless Communications
Prof. Sundeep rangan

## Slide 2: Outline
Antenna Arrays and the Spatial Signature
Receive Beamforming and SNR Gain with a Single Path
Array Factor
Transmit Beamforming with a Single Path
Multipath and MIMO Channels
Linear Algebra and SVD Review
Beamforming Gains in Multipath Channels
Adding Element Gains and Normalizing Spatial Signatures for Mutual Coupling

## Slide 3: Antenna Arrays
Antenna arrays: Structure with multiple antennas
  At TX and/or RX
  Key to 5G mmWave and massive MIMO
Two key benefits
Beamforming: This lecture
  Concentrate power in particular directions
  Increases SNR and may enable spatial diversity
  Requires arrays at either TX or RX
Spatial multiplexing: Later
  Enables transmission in multiple virtual paths
  Increases degrees of freedom
  Requires multiple antennas at both TX and RX
IBM 28 GHz array
32 element dual polarized array Sadhu et al, ISSCC 2017
Aurora C-Band Massive MIMO array
64 elements, 5-6 GHz
https://www.taoglas.com/

## Slide 4: Multiple Receive Antennas
Single Input Multiple Output
  One TX antenna
  RX antennas
Transmit a scalar signal
Receive a vector of signals:
What is the channel from to ?
Want channel in complex baseband

## Slide 5: Channel vs. Position
Consider single path channel that arrives at origin with:
  Delay , complex gain , AoA of relative to z-axis
Transmit signal
Look at RX signal as a function of position
Assume RX position, is close to origin
  bandwidth of
Phase rotation with displacement:
  Baseband response at is (proof on next slide):
RX position
Response at
Phase rotation with

## Slide 6: Proof of Phase Rotation with Displacement
Delay of path at is:
Hence there is an additional delay:
Baseband response at :
Also, if
But, by assumption of small displacement:
Hence,
RX position

## Slide 7: Response for a ULA
Uniform Linear array (ULA)
  antenna positions spaced apart
Transmit signal
  Channel single path with AoA , complex gain
Response at position:
In vector notation, we can write
  is the channel vector

## Slide 8: Response Decomposition
For a single path channel, the channel vector has two components:
Scalar channel gain,
  Complex channel gain at a reference position in the array
Vector spatial signature,
  Vector of phase shifts from the reference
  Also called the steering vector (reason for name will be clear later)

## Slide 9: Array Response in 3D
Many arrays place elements over 2D area
Uniform rectangular array (URA):
  grid of elements
  Spaced and
  Also called uniform planar array (UPA)
Incident angle
  (Azimuth, elevation) or (azimuth, inclination)
Spatial signature:
  complex response to antenna

## Slide 10: Mutual Coupling
The above formulas assume there is no mutual coupling
Mutual coupling:
  Signals on one antenna scatter to another antenna
  Changes the antenna response
Mutual coupling effect is typically large when:
  Antennas are close
  Or arrays are combined with highly directive elements
We will show how to account for mutual coupling at the end of unit
Wang, Zhengzheng. “Complete tool for predicting the mutual coupling in non-uniform arrays of rectangular aperture radiators.” (2017).

## Slide 11: MATLAB Phased Array Toolbox
Powerful toolbox
Routines for:
  Defining and visualizing arrays
  Computing beam patterns
  Beamforming
  MIMO
  Radar
  …

## Slide 12: Example: Defining a ULA
Define and view the array
Can display array:
  Using viewArray command
  Or, manually

## Slide 13: Computing the Spatial Signature
Compute the spatial signature with the SteeringVector object

## Slide 14: Example: Defining a URA
Define and view the array
Use the phased.URA class
Can compute steering vector similarly
A 4 x 8 URA with normal axis aligned on x

## Slide 15: Multiple Antennas in Commercial Systems
Sub 6 GHz systems: Mostly 1 to 4 antennas on base stations or smart phones
Form factor restricts larger number of antennas
WiFi Router
Linksys AC2200 with 4TX/RX
2x2 LTE base station antenna
Cros-polarization
16 dBi element gain, 90 deg sector 750x120x60mm
K. Zhao, S. Zhang, K. Ishimiya, Z. Ying and S. He, "Body-Insensitive Multimode MIMO Terminal Antenna of Double-Ring Structure," in IEEE Transactions on Antennas and Propagation, vol. 63, no. 5, pp. 1925-1936, May 2015.

## Slide 16: Massive MIMO
Massive MIMO:
  Many base station antennas
  64 to 128 in many systems today
Significant capacity increase
  Typically 8x by most estimates
Use SDMA
  Will discuss this later

## Slide 17: Beamforming and MmWave
To compensate for high isotropic path loss, mmWave systems need large number of antennas
5G handsets: Multiple arrays with 4 to 8 antennas each
5G base stations: 64 to 256 elements
IBM 28 GHz array
32 element dual polarized array Sadhu et al, ISSCC 2017
Huo, Yiming, et al. "Cellular and WiFi co-design for 5G user equipment." 2018 IEEE 5G World Forum (5GWF). IEEE, 2018.

## Slide 18: Outline
Antenna Arrays and the Spatial Signature
Receive Beamforming and SNR Gain with a Single Path
Array Factor
Transmit Beamforming with a Single Path
Multipath and MIMO Channels
Linear Algebra and SVD Review
Beamforming Gains in Multipath Channels
Adding Element Gains and Normalizing Spatial Signatures for Mutual Coupling

## Slide 19: RX Beamforming
Consider a general channel:
  1 input, M outputs
Beamforming: Take a linear combination of signals
  is called beamforming vector for multiple antennas
Creates effective SISO channel:
  1 input 1 output symbol
  Gain:
  Noise:
X
X
+

## Slide 20: Conjugate Transpose Conventions
For beamforming, we will use the following conventions
Complex conjugate of a complex scalar is denoted
Unless otherwise specified, vectors are column vectors:
Transpose:
Conjugate transpose:
Elementwise conjugate:
  Takes conjugate of each element but keeps a column vector

## Slide 21: Beamforming Analysis
Linear combining:
  Gain:
  Noise:
Analysis: Let
  average symbol energy
  Assume noise (i.i.d. complex Gaussian noise)
Then, after combining;
  Signal energy
  Noise: is Gaussian with
  SNR is:

## Slide 22: Maximum Ratio Combining
From previous slide: SNR is
Maximum ratio combining: Select BF vector to maximize SNR:
Theorem: The MRC weighting vector and maximum SNR is:
  Any constant can be used. Constant does not matter
  Align BF vector with the conjugate of the channel
Also called conjugate beamforming

## Slide 23: Proof of the MRC Solution
We want to maximize
Write the inner product as:
Hence, we want to maximize
From Cauchy-Schwartz:
  Hence,
  Maximized with
So, we take
Double conjugate

## Slide 24: MRC Gain
SNR with MRC:
SNR on channel is:
Average SNR is:
MRC increases SNR by a factor of relative to average per channel SNR
Beamforming gain =
Example: Suppose average SNR per antenna is 10 dB.
  With antennas and MRC, SNR dB
  Gain increases significantly!
Note: The gain assumes no mutual coupling.
  Once antennas are close, the gain will no longer increase by

## Slide 25: Single Path Channel Case
Consider special case of single path channel:
  Channel is
SNR per antenna (before beamforming):
  Assume includes only phase shifts
SNR after BF:
MRC beamforming: and
Conclusions:
  Optimal (MRC) beamforming vector is aligned to the conjugate of the spatial signature
  Optimal SNR gain (assuming no mutual coupling)
  Linear gain with number of antennas

## Slide 26: Example Problem
Consider a system
  TX power = 23 dBm with antenna directivity = 10 dBi
  Free space path loss 1000 m
  Sample rate = 400 Msym/s
  Noise energy = -170 dBm/Hz (including NF)
  RX antenna directivity = 5 dBi and 8 elements
Find SNR per antenna and SNR with MRC
Solution: We get a 9 dB gain!

## Slide 27: In-Class Problem: Simple QPSK simulation
Simulate QPSK transmission over a single path channel

## Slide 28: Outline
Antenna Arrays and the Spatial Signature
Receive Beamforming and SNR Gain with a Single Path
Array Factor
Transmit Beamforming with a Single Path
Multipath and MIMO Channels
Linear Algebra and SVD Review
Beamforming Gains in Multipath Channels
Adding Element Gains and Normalizing Spatial Signatures for Mutual Coupling

## Slide 29: Array Factor
Suppose RX aligns antenna for AoA
But signal arrives from AoA
Define the (complex) array factor
  Assume
  Indicates directional gain as a function of AoA
  Dependence on often omitted
SNR gain =
  Max value =
  Usually measured in dBi (dB relative to isotropic)
  Also called the array response
Actual arrival
BF direction
Array

## Slide 30: Uniform Linear Array
Spatial signature (for azimuth angle ):
  Note change from to . (Array aligned on y-axis)
Optimal BF vector for AoA
  (Note normalization)
Array factor:
  ,
Antenna gain:
Arrival
BF direction

## Slide 31: Antenna Gain for ULA
Maximum gain of
Note:
  Endfire vs. broadside
  Beamwidth
Broadside:
Endfire:

## Slide 32: Plotting the Array Factor
Create a SteeringVector object
Get steering vectors
Compute inner products

## Slide 33: Polar Plot
Useful to visualize in polar plot
Note key features:
  Direction of maximum gain
  Sidelobes
  Pattern repeated on reverse side

## Slide 34: Key Statistics
From Jacobs University slides
Values in () for:
Full null beamwidth (zero to zero)
Half power beamwidth (-3dB to -3dB)
First sidelobe level

## Slide 35: Grating Lobes
When
Obtain multiple peaks
Does not direct gain in one direction

## Slide 36: Plotting the Patterns
MATLAB has excellent routines for 3D patterns
Note that this plots directivity not array factor

## Slide 37: Outline
Antenna Arrays and the Spatial Signature
Receive Beamforming and SNR Gain with a Single Path
Array Factor
Transmit Beamforming with a Single Path
Multipath and MIMO Channels
Linear Algebra and SVD Review
Beamforming Gains in Multipath Channels
Adding Element Gains and Normalizing Spatial Signatures for Mutual Coupling

## Slide 38: Multiple TX antennas
MISO channel
  Multiple input single output
  TX antennas, 1 RX antennas
  Transmit vector:
  Scalar RX:
Most of the theory is identical to the SIMO channel

## Slide 39: Single Path Channel
First consider single path channel
Similar to the SIMO case, RX signal is:
  path gain
  = angle of departure
  = path delay
  TX spatial signature
  : complex TX element gain
TX and RX spatial signatures are identical
TX array
RX with single antenna

## Slide 40: TX Beamforming
RX signal is:
TX beamforming
  Input scalar information signal
  Create vector signal to antennas:
Signal to antenna is:
  is a complex weight applied to signal
is called the TX beamforming vector
  Also called pre-coding
TX array
RX
signals
Scalar
TX BF vector

## Slide 41: SNR with TX Beamforming
RX signal is:
  Drop dependence on time to simplify notation
With SISO channel is
Total transmitted energy across all TX chains is:
  To keep constant total energy:
  Assumes no mutual coupling
SNR is
  is the SNR for a single antenna
TX array
RX
signals
Scalar
TX BF vector

## Slide 42: MRC TX Beamforming
From previous slide, SNR is:
To maximize SNR s.t. power constraint
MRC TX BF vector:
  Align with the conjugate of the spatial signature
  SNR gain
Define and compute Array Factor similarly
TX array
RX
signals
Scalar
TX BF vector

## Slide 43: Outline
Antenna Arrays and the Spatial Signature
Receive Beamforming and SNR Gain with a Single Path
Array Factor
Transmit Beamforming with a Single Path
Multipath and MIMO Channels
Linear Algebra and SVD Review
Beamforming Gains in Multipath Channels
Adding Element Gains and Normalizing Spatial Signatures for Mutual Coupling

## Slide 44: MIMO Channel with a Single Path
Multi-input Multi-Output (MIMO) channel:
  TX array with elements
  RX array with elements
Single path channel:
MIMO channel matrix for a single path channel:
TX array
RX array

## Slide 45: Beamforming on a MIMO Channel
Consider MIMO channel, ,
  Channel on time and frequency resource
Apply TX beamforming:
  Assume so total transmit energy is
Apply RX beamforming:
  Assume so total received noise energy
Equivalent channel:
  complex beamformed channel gain
  Noise energy is
SNR with beamforming:

## Slide 46: Beamforming Gain with a Single Path
From previous slide, we saw SNR on a MIMO channel is:
Suppose we have a single path channel:
Take TX and RX conjugate beamforming vectors:
Then SNR is
But is the SNR per antenna
Conclusion: Maximum BF gain on a single path channel is
  Again, assuming no mutual coupling

## Slide 47: Friis’ Law and MmWave
Recall Friis’ Law:
Isotropic path loss decreases with
Millimeter Wave systems: Increases
  Decreases Increase path loss
But, with beamforming:
  Directivity and
  Each antenna takes area
  So, for fixed total aperture:
Can compensate isotropic path loss with directivity

## Slide 48: Friis’ Law and MmWave
Friis’ Law:
Conclusions: With a fixed aperture and beamforming
  Isotropic path loss can be overcome
But systems need very directive beams
  Raises many other issues. E.g. Channel tracking, processing, …
Condition | Directivity scaling | Path loss scaling
No beamforming | constant | 
Beamforming on one side (TX or RX) | constant | constant
Beamforming on both sides (TX and RX) |  | 
Condition | Directivity scaling | Path loss scaling
No beamforming |  | 
Beamforming on one side (TX or RX) |  | 
Beamforming on both sides (TX and RX) |  | 

## Slide 49: Multiple Paths
Easy to extend channel response to multiple paths
Each path adds a term with a spatial signature
Time-domain model
Complex gain
Doppler shift
AoA
Delay
AoD

## Slide 50: Time-Varying Frequency Response
The channel response can also be described as a time and frequency-varying matrix
  At time and frequency
  Varies in time due to Doppler shifts
  Varies in frequency due to delay spread

## Slide 51: OFDM Time-Frequency Grid
Consider OFDM channel
  Sub-carrier spacing , symbol time
  Index with OFDM symbol index, = subcarrier index
Transmit array:
  At each , we transmit a vector
  number of TX antennas
Receive array:
  number of RX antennas
  One dim vector per resource element
Subcarrier spacing
OFDM symbol
Time
Frequency

## Slide 52: OFDM Channel with Multiple RX Antennas
OFDM channel acts as multiplication:
Under normal operation (delay spread is contained in CP):
OFDM channel gains can be computed from the multi-path components
  OFDM symbol time, sub-carrier spacing
  For each path: Doppler shift, Delay, complex gain
RX symbol vector
Channel matrix
TX symbol vector

## Slide 53: Outline
Antenna Arrays and the Spatial Signature
Receive Beamforming and SNR Gain with a Single Path
Array Factor
Transmit Beamforming with a Single Path
Multipath and MIMO Channels
Linear Algebra and SVD Review
Beamforming Gains in Multipath Channels
Adding Element Gains and Normalizing Spatial Signatures for Mutual Coupling

## Slide 54: Orthogonal Vectors
Let or (real or complex)
Vectors are orthogonal if .
  Write
  Visually, if they are at 90 degrees
A set of vectors are orthonormal
  when
  for all
  Vectors are pairwise orthogonal and unit norm
Orthonormal basis: An orthonormal set
  Any vector can be written
  are the coefficients of in the basis

## Slide 55: Orthogonal and Unitary Matrices
A matrix is unitary if
A matrix is orthogonal if
  Orthogonal is just the real-valued version of unitary
Key properties:
  is orthogonal if and only if columns are orthonormal
  is orthogonal if and only if rows are orthonormal
  Taking an inverse is easy

## Slide 56: Examples of Orthogonal Matrices
2D rotation matrix by :
  Can verify that
  3D rotation matrices are also orthogonal
Example with 3 vectors:
  Let
  Can verify that
  Hence the matrix:

## Slide 57: Beamspace Matrices
Consider a ULA with normalized steering vector:
Take angles:
  This is possible if
The vectors are orthonormal
These are called the beamspace vectors
  An orthonormal basis for the spatial domain

## Slide 58: Symmetric and Hermitian Matrices
Definition:
  A matrix is symmetric if
  A matrix is Hermitian if
Symmetric is the real version of Hermitian
For any symmetric / Hermitian:
  There are an orthonormal set of eigenvectors with eigenvalues
  All eigenvalues are real (not complex)
Let = Matrix with the eigenvectors as the columns
  Then is orthogonal / unitary
  Hence diagonalizable with unitary

## Slide 59: Sample Problem
Let . Find an orthogonal bases of eigenvectors and their eigenvalues
Solution: Eigenvalues:
For
  Take
For
  Take

## Slide 60: Positive Definite Matrices
Let be symmetric / Hermitian with eigenvalues
  Recall that the eigenvalues are real
Definition:
  is positive semi-definite if for all
  is positive definite if for all
Notation: for positive definite and when is positive semi-definite
Key property: If then:
  if and only if for all
  if and only if for all

## Slide 61: Matrix Square Roots
Theorem: Let Then if and only if for some
  Note: The dimension can be anything or
Proof:
  Suppose . Then
  Write .
  Then:
  Since and , is called the matrix square root. Write
  Suppose .
  Then for any

## Slide 62: Singular Value Decomposition
Given matrix , an SVD is a factorization of the form, where
  , a unitary matrix
  , a unitary matrix
  If , . If ,
Values Called the singular values
All matrices have an SVD
“Tall” ,
“Fat” ,
Notes: SVD is a powerful techniuque in all kinds of numerical linear algebra/ml/etc.
It's just a way to compute principal component analysis
SVD is kind of like an eigenvalue decomposition that it factors the matrix into three parts.
S is diagonal, rxr, sorted called singular values.
All marix in universe has svd. Even if not square.

## Slide 63: Example
Let
Then can check that
  Also verify that and
  This can be found by (cleverly) permute the rows of
  But, in general, use a computer to compute SVD

## Slide 64: Geometric Interpretation
Let and
Consider a transformed space
  so are the coefficients of the input in the basis
  so are the coefficients in the basis
Then: so
Each input direction is mapped to
Consequence:
  SVD finds orthonormal bases such that matrix is a linear scaling in each basis vector
A
A

## Slide 65: SVD and Rank
Theorem: Suppose , then num of positive singular values
Ex: Suppose with
  Then:
Proof:
  For any the output is
  Define and
  Then
  If then for
  Hence, by varying , we can span a space of dimension
65
A
A

## Slide 66: Sum of Rank One Form
Suppose with
Then:
  A sum of rank one terms
The vectors are an orthonormal basis for
The vectors are an orthonormal basis for

## Slide 67: Outline
Antenna Arrays and the Spatial Signature
Receive Beamforming and SNR Gain with a Single Path
Array Factor
Transmit Beamforming with a Single Path
Multipath and MIMO Channels
Linear Algebra and SVD Review
Beamforming Gains in Multipath Channels
Adding Element Gains and Normalizing Spatial Signatures for Mutual Coupling

## Slide 68: SVD of the Channel Matrix
Consider a MIMO channel matrix:
  RX energy per antenna on path
  phase that varies with frequency and time
We can write this as: where
  and = normalized steering vectors
Interpretation:
  number of paths = rank of
  If the signatures and are orthogonal then they are the left and right singular vectors
  In this case, singular values squared RX energy beamforming gain

## Slide 69: Beamforming on a MIMO Channel
Consider MIMO channel, ,
  Channel on time and frequency resource
Apply TX beamforming:
  Assume so total transmit energy is
Apply RX beamforming:
  Assume so total received noise energy
Equivalent channel:
  complex beamformed channel gain
  Noise energy is
SNR with beamforming:

## Slide 70: Maximizing the SNR
From previous slide, MIMO channel with beamforming is
  Gain:
  Noise energy
  SNR:
Want to select the beamforming vectors to maximize the SNR:
Theorem: Let be the SVD. Then, then the optimal vectors are
  conjugate of the left singular vector for maximal singular value
  conjugate of the right singular vector for maximal singular value
  Also, the max value is maximum singular value squared

## Slide 71: CSI Requirements
Optimal BF vectors are maximal singular vectors of channel matrix
Problem: TX and RX must know exactly
  Channel state information (CSI) must be available at TX and RX
  In general, varies with time and frequency
  Hence channel needs to be tracked!
Next lecture we will discuss:
  How to track channel in practical systems
  Methods to approximate beamforming if exact tracking is not possible

## Slide 72: Outline
Antenna Arrays and the Spatial Signature
Receive Beamforming and SNR Gain with a Single Path
Array Factor
Transmit Beamforming with a Single Path
Multipath and MIMO Channels
Linear Algebra and SVD Review
Beamforming Gains in Multipath Channels
Adding Element Gains and Normalizing Spatial Signatures for Mutual Coupling

## Slide 73: Modeling the Element Pattern
Above analysis assumes each element is omni-directional
However, in most systems, each antenna element may also have gain.
In this section, we describe two methods to account for element gain
Method 1. Pattern multiplication without normalization
  Provides a simple approximation of the channel response
  But neglects mutual coupling
Method 2. Pattern multiplication with normalization
  More accurate
  Partially accounts for mutual coupling
SiBeam 60 GHz array
12 TX and 12 RX elements.

## Slide 74: Uncoupled Array Assumption
Consider a TX array with elements in free space
  Analysis for RX is similar
In isolation, we know each TX signal will produce an RX signal
  free space path gain from a reference location
  phase shift due to the element location relative to reference
  complex element gain (assumed common for all elements)
Uncoupled array assumption:
  The response from the antennas together is given by super-position
  This is the assumption we have made implicitly up to now
TX array
RX

## Slide 75: Pattern Multiplication
Previous slide shows that ignoring mutual coupling, the TX channel response is:
We call the pattern multiplication signature or un-normalized spatial signature
  Multiplication of the array spatial signature with the element pattern
Key properties:
  TX channel is
  Optimal BF vector
  Optimal BF gain |peak element gain peak array gain
  Array factor is

## Slide 76: Impedance and Resistance Matrices
To model mutual coupling, we need some simple network theory
The input to an array can be modeled as an port network
  Each “port” has an input current and voltage
  Physically, the port would be the antenna feed
  The currents and voltages are represented in complex baseband
Any port network is characterized by an impedance matrix
  and are the vector of currents and voltages
  The impedance matrix accounts for coupling between ports
The real power consumed in the network is
  Hermitian part of . Called the resistance matrix
Coupling

## Slide 77: Normalized Steering Vector
To account for coupling between antennas, define the normalized spatial signature
  is a scaled version of the spatial signature with pattern multiplication
  is called the normalization matrix, inverse of the matrix square root
Theorem: The TX channel in free space is
  Recall, is the free space channel from the reference point in the array
  Proved below using network theory
Conclusion: represents the array response
  Properly accounts for coupling between elements
TX array
RX

## Slide 78: Normalized Channel Response
Theorem: There exists a constant such that if :
  The total transmitted power is
  The received signal at a point in free space is where is the free space SISO channel
  Received power is
Proof: Will be done in several slides below
Conclusion: represents the effective array response
  Properly accounts for coupling between elements
  Based on a transformation of the signals to array
TX array
RX

## Slide 79: Numerical Procedure for Normalization
Get angles uniformly in
Get steering vectors and element gain at each angle
Compute normalization matrix:
  Scale factor used to normalize the summation
The normalized steering vector at any new angle is
The complex gain with beamforming vector is
  Power gain

## Slide 80: Array Element Example
Element:
  Patch Microstrip
  Max gain 10 dBi gain
Array: 4x4 URA
  Max gain = dBi
  Has directivity in back and front

## Slide 81: Array Factor Examples
For each target angle:
  Find optimal BF vector
  Compute resulting array factor
Array factor computed for
  No normalization (approximate)
  Normalization
We see approximation is close
  But overestimates peak gain
No normalization
Normalization
Target angle

## Slide 82: Max Gain
Plotted:
  Max gain in each angle
With no normalization:
  Max gain at boresight dBi
With normalization:
  Max gain at boresight18.3 dBi
  Max gain at other angles more uniform

## Slide 83: Proof Part 1: Analyzing in Current Domain
Let vector of complex baseband current inputs to the antennas
Consider electric field at angle at far distance
Assume the electric field from a single current is:
  some proportionality constant
We know super-position applies for currents
  This is a consequence of Maxwell’s equations
Hence with all currents:
TX antenna

## Slide 84: Proof Part 2: Total Radiated Power
From previous slide: Electric field is
Hence, power intensity is
  characteristic impedance
Hence, the total radiated power is:
Here
elementwise complex conjugate of
TX array
RX

## Slide 85: Proof Part 3: Array Resistance Matrix
From previous slide we saw that :
  can be computed from the integral of spatial signatures
We know from network theory the power consumed is
  = resistance matrix of the array
If the antennas are lossless, this power must be transmitted
Hence
Conclusions:
  The matrix is a scaled version of the antenna array resistance matrix
  The matrix captures the coupling of currents and voltages between antennas
Coupling

## Slide 86: Proof Part 4: Computing the Channel
Up to now we have shown:
  Total transmitted power is
  Radiation intensity at angle is
Define:
  Power input vector:
  Normalized steering vector:
With these definitions:
  Total transmitted power is
  Radiation intensity at angle is
Hence is the power gain relative to free space propagation
Therefore, channel can be modeled as is the free space channel